## Slide 1: This Time Lecture Outline – ISAs
Write 3AC code for the following program
int v(int a, int b){
if (a > 1){
if (b < 3){
return a + b;
}
}
}

## Slide 2: Last Time Lecture Review - Runtimes
Runtimes
Runtime Environments
Tradeoff between what’s done
dynamically vs statically
Hardware Intuition
Memory is a big 1D array
Runtime
Environments
You Should Know
Different runtime environment types
  Advantages/Disadvantages
Compiling vs Interpreting
Instruction Set Architectures
Drew Davidson | University of Kansas

## Slide 3: Last Time Lecture Review - Runtimes
Runtimes
Runtime Environments
Tradeoff between what’s done
dynamically vs statically
Hardware Intuition
Memory is a big 1D array
Runtime
Environments
You Should Know
Different runtime environment types
  Advantages/Disadvantages
Compiling vs Interpreting

## Slide 4: This Time Lecture Outline – ISAs
Instruction-Set Architectures
Introduction
What an ISA does
Our target ISA: x64
Writing x64
Architecture

## Slide 5: Hardware Capabilities ISAs - Intro
Computers can store binary sequences in memory
An entire program thus needs to be mapped to binary sequences
Electrical
Engineers
0s and 1s
Computer
Scientists

## Slide 6: W.Y.S.I.N.W.Y.X ISAs - Introduction
What You See (in source code) Is Not What You eXecute
  Many of our abstractions lack explicit representation in machine code

## Slide 7: Hardware Generally Has… ISAs - Introduction
Limited number of very fast registers with which to do computation
Comparatively large region of memory to hold data
Some basic instructions from which to build more complex behaviors

## Slide 8: Missing Abstractions of Machine Code ISAs - Introduction
Loops
Expressions
Variables
Scope
Functions
Opcodes
Registers
Byte-addressable
memory

## Slide 9: Programs as Numeric Sequences ISAs - Introduction
We gotta encode the whole dang program into a 1D-array!
Encode data as binary sequences
Encode instructions as binary sequences
Need to use the
same space for
many things
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0007
0x0008
0x0009
0x000A
0x0006
0x44
0x01
0x00
0x00
0x00
0x03
Address
Address
Address
Address
Address
Address
Address
Address
Address
Address
0x07
0x44
0x01
0x03
0x02

## Slide 10: Memory: Intuition ISAs – Hardware Features
Cells have a (numeric) address and hold (numeric) value
We can think of program memory as a big ol’ 1D-array
Data access is like indexing into that array
[a] := [b]
memory[a]
memory[b]
a
b
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0006
Address
Address
Address
Address
Address
Address
0x4
0x2
0x3
0x4
0x6
0x2
0x5
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0006
Address
Address
Address
Address
Address
Address
a
b
0x3
0x2
0x3
0x4
0x6
0x2
0x5
assume a takes up address 0x0001
assume b takes up address 0x0005

## Slide 11: Registers: Intuition ISAs – Hardware Features
Specialized, super-fast circuitry
Computation must be done on registers
Get operand 1 into a register
Get operand 2 into another register
Sum the two registers to a destination register
Store destination register back to memory
[a] := [b] + [c]
Corresponding Hardware tasks
3AC code
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0007
0x0008
0x0009
0x000A
0x0006
0x44
0x01
0x00
0x00
0x00
0x03
Address
Address
Address
Address
Address
Address
Address
Address
Address
Address
0x07
0x44
0x01
0x03
0x02
Memory: “data at rest”
Registers: “data in flight”

## Slide 12: This Time Lecture Outline – ISA Hardware Features
Instruction-Set Architectures
Introduction
What an ISA does
Our target ISA: x64
Writing x64
Architecture

## Slide 13: Processors Conform to ISAs ISAs – Hardware Features
Upon encountering a byte sequence an ISA-conformant “knows” how to interpret the sequence
Still has some flexibility on how to execute it, specified via the microarchitecture
You’re speakin’ my language!

## Slide 14: The ISA Contract ISAs - Intro
Hardware
Software
ISA: A contract of hardware aspects
An ISA specifies
How data is encoded
Instructions that can transform data
Opcodes for how instructions are encoded
Program state

## Slide 15: Instruction Set Architectures ISAs - Intro
Hypothetical ISA
-2 is encoded as 1110
-1 is encoded as 1111
8 is encoded as 1000
12 is encoded as 1100
The INC_ADDR <X> instruction
increments the value at
memory address <X>
INC_ADDR 8 is encoded as 1010
Next instruction to execute
is stored in register I
An ISA specifies
How data is encoded
Instructions that can transform data
Opcodes for how instructions are encoded
Program state

## Slide 16: Completely Hypothetical ISA Example ISAs - Intro
Address
0x8
0x9
0xA
0xB
0xC
0xD
0xF
0xE
1
1
0
Address
Address
Address
Address
Address
Address
Address
1
0
1
0
1
…
…
0x10
0x12
0x14
0x13
0
Address
Address
Address
Address
1
1
0
-2 is encoded as 1110
-1 is encoded as 1111
8 is encoded as 1000
12 is encoded as 1100
The INC_ADDR <X>
increments the value at
memory address <X>
INC_ADDR 8
encoded as
1010
Next instruction
to execute
stored in Register K
Register K:
1100
1
1
1
1
Execute: the value at
address 8 is -2
Decode: the 4-bit instruction at address 12 is INC_ADDR 8
Fetch: the instruction at address 12

## Slide 17: More Realistic Encodings ISAs - Intro
The previous ISA uses unrealistic encodings
Let’s consider some more likely choices

## Slide 18: Encoding Data: Granularity of Access ISAs - Intro
How “big” is a memory cell?
Bit-addressable
Let’s say we’re storing the byte 0x61 = 01100001
Byte-addressable
Could even go bigger?
But why (and why not)?
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0007
0x0008
0x0009
0x000A
0x0006
0
1
0
0
0
0
Address
Address
Address
Address
Address
Address
Address
Address
Address
Address
0
0
0
1
0
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0007
0x0008
0x0009
0x000A
0x0006
0x44
0x01
0x00
0x00
0x00
0x03
Address
Address
Address
Address
Address
Address
Address
Address
Address
Address
0x07
0x44
0x01
0x03
0x02

## Slide 19: Data Encodings ISAs - Intro
You should already know the basic idea here
Type dictates numeric representation
Devote a certain size (in bits) to representation
Use binary hardware to store the numeric value
0x43
‘C’
0x434F4F41
0x4F
0x4F
0x4C
0100 0011
0100 1111
0100 1111
0100 1100
‘O’
‘O’
‘L’
1,129,271,105‬
Bit Sequence (binary)
Byte Sequence (Hex)
ASCII Value: char type (8 bits, i.e. 1 byte)
Integer Value: int32 type (32 bits, i.e. 4 bytes)

## Slide 20: Convention: Memory Regions ISAs - Intro
Portions of memory “zoned” by purpose
Simplest form:
  Code region
  Data region
  The rest is free space
Address
0x0000
0x0001
0x0002
0x0003
0x0004
0x0005
0x0007
0x0008
0x0009
0x000A
0x0006
Address
Address
Address
Address
Address
Address
Address
Address
Address
Address
Memory
code
data
free

## Slide 21: Data Sub-Regions ISAs - Intro
Further break up data region for different kinds of data
Global variables
Local variables
Objects

## Slide 22: This Time Lecture Outline – About x64
Instruction-Set Architectures
Introduction
What an ISA does
Our target ISA: x64
Writing x64
Architecture

## Slide 23: Our ISA: x64 Lecture Outline – About x64
Probably the most popular architecture in modern use
Almost certainly what your computer is running
Definitely what the cycle servers are running

## Slide 24: x86 and x64: A Reputation for Difficulty Lecture Outline – About x64
Highly complex instruction set
~1000 different instructions via the most conservative count*
Some instructions context-sensitive (i.e. work differently based on preceding instructions)
*that we don’t have a canonical
instruction count
is already a pretty bad sign

## Slide 25: x64 Registers Lecture Outline – About x64
Name | Number | Nominal Purpose
rax | 0 | Computation Accumulator
rbx | 1 | Computation Base
rcx | 2 | Computation counter
rdx | 3 | Data for I/O
rsi | 4 | String source address
rdi | 5 | String destination address
rbp | 6 | Base pointer (base of the stack)
rsp | 7 | Stack pointer (edge of the stack)
r08 – r15 | 8 - 15 | True general purpose registers
rip | - | Instruction pointer
rflags | - | Status flags
Can be used in
Instruction opcodes
Cannot be used in
instruction opcodes

## Slide 26: x64 Register Compatibility Lecture Outline – About x64
Register #0 – the “A” register
rax
eax
ax
al
ah
byte 8
byte 7
byte 6
byte 5
byte 4
byte 3
byte 2
byte 1
64
32
16
8

## Slide 27: This Time Lecture Outline – Writing x64
Instruction-Set Architectures
Introduction
What an ISA does
Our target ISA: x64
Writing x64
Architecture

## Slide 28: Stepping Back From Binary Lecture Outline –Writing x64
Dealing with binary directly is tedious and error-prone
Laying out code / data is super difficult to do manually
Remembering the binary opcode sequence for every instruction is difficult
Fortunately, we don’t have to do that

## Slide 29: The Assembler Lecture Outline –Writing x64
Write low-level textual mnemonics (assembly code)
Assembly code isn’t directly executable
Nearly 1-1 with the binary encoding
Different assemblers, different syntax
Compiler
Assembler
Code

## Slide 30: ASM Instruction Syntax Lecture Outline –Writing x64
As with everything x86-related, it’s complicated
We’ll use the AT&T Syntax:
  <opcode><sizesuffix> <src operand(s)> <dst operand>
Immediates (i.e. constant values) prefixed by $
Registers prefixed by %
Memory lookup (i.e. dereference) in parens
movq $5, (%rax)
mov the 64-bit value 5 into the 64-bit
memory address specified by register rax

## Slide 31: Directives Lecture Outline –Writing x64
Indicates a command to the assembler
  Layout, program entrypoint, etc.
Example:
.globl X
Indicates that symbol X is visible outside of the file

## Slide 32: Segment Directives Lecture Outline –Writing x64
.data
Lay out items in the data segment
.text
Lay out items in the user text segment
Instructions go here
Globals go here

## Slide 33: Labels Lecture Outline –Writing x64
The assembler allows us to specify “placeholder” addresses that will be used later
  Translated to “real” addresses by a utility called the linker
Valid for both data and code locations
jmp 0x12d34a5678a
jmp LBL1
…
LBL1: movq $5 (%rax)

## Slide 34: System Calls Lecture Outline –Writing x64
To interact outside program memory, need the help of the OS
%rax # Which system call (60 is exit)
%rdi # Set syscall arg – (exit takes the return code)
syscall

## Slide 35: Time to put it all together! Lecture Outline –Writing x64
Photo Credit: Tim Klein - https://puzzlemontage.crevado.com

## Slide 36: A Complete Program Lecture Outline –Writing x64
.text
.globl _start _start: movq $60, %rax # Choose syscall exit movq $4, %rdi # Set syscall arg - return code
syscall

## Slide 37: Actually Running a Program Lecture Outline –Writing x64
Invoking the assembler and linker
as –o start.o start.s
ld start.o –o prog
./prog
echo $?

## Slide 38: Summary ISAs
ISAs
Provide an interface from software to hardware
We’ll target assembly code, assembler will take it from there
X64
A popular architecture
We’ve covered the basic instruction format and a simple program

## Slide 39: Next Time ISAs
We’ll dive into more details about X64